## Slide 1
UART TX/RX IP Core
FSM-Based RTL Design and Loopback Verification
VLSI Internship Project
Verilog RTL • Verilator • EPWave
UART TX/RX IP Core | VLSI Internship Project 1

## Slide 2
Project Description
Objective and scope
• Design and verify a UART transmitter and receiver as reusable RTL IP blocks.
• Implement the standard 8-N-1 UART frame: 1 start bit, 8 data bits, no parity and 1 stop bit.
• Use finite-state machines to control transmission, reception, bit counting and timing.
• Provide parameterized bit timing through CLKS_PER_BIT.
• Verify the design through loopback simulation using Verilator and EPWave.
UART TX/RX IP Core | VLSI Internship Project 2

## Slide 3
UART IP Architecture
Separate TX and RX FSMs connected through a serial loopback path
TX FSM
Parallel data → serial TX
Serial Link
UART TX line / loopback
RX FSM
Serial RX → parallel data
• TX states: IDLE → START → DATA → STOP
• RX states: IDLE → START → DATA → STOP
• Bit counters track the eight data bits; clock counters define bit timing.
• Loopback connects TX directly to RX for end-to-end verification.
UART TX/RX IP Core | VLSI Internship Project 3

## Slide 4
UART Frame Format & Operation
8-N-1 serial communication
START
0
D0
1
D1
0
D2
1
D3
0
D4
0
D5
1
D6
0
D7
1
STOP
1
• UART line is idle-high; a low start bit marks the beginning of a frame.
• Data is transmitted least-significant bit first.
• The receiver detects the start bit, samples the eight data bits and checks the stop bit.
• rx_valid pulses when a complete and valid byte has been reconstructed.
UART TX/RX IP Core | VLSI Internship Project 4

## Slide 5
Tools & Verification Methodology
RTL design → simulation → waveform analysis
1
Verilog RTL
Implemented UART TX/RX FSMs with parameterized timing.
2
Testbench
Generated clock, reset and two loopback data transactions.
3
Verilator 5.044
Compiled and simulated the design.
4
VCD Trace
Captured internal and external signal activity.
5
EPWave
Analyzed TX/RX data, FSM states and bit counters.
UART TX/RX IP Core | VLSI Internship Project 5

## Slide 6
Simulation Test Cases
Loopback verification of two independent data patterns
Test | TX Data | RX Data | Result
1 | 0xA5 | 0xA5 | PASS
2 | 0x3C | 0x3C | PASS
• Both transmitted bytes were reconstructed correctly by the receiver.
• rx_valid asserted after successful reception of each byte.
• Verilator completed the simulation without compilation warnings or errors.
UART TX/RX IP Core | VLSI Internship Project 6

## Slide 7
Simulation Result – Detailed FSM Waveform
EPWave view of UART timing, state transitions and bit counters
TX/RX FSMs progress through IDLE → START → DATA → STOP while bit and clock counters control the transfer.
UART TX/RX IP Core | VLSI Internship Project 7

## Slide 8
Simulation Result – End-to-End Loopback
Complete simulation showing successful reception of 0xA5 and 0x3C
rx_data changes to A5 and 3C, with rx_valid pulsing after each complete UART frame.
UART TX/RX IP Core | VLSI Internship Project 8

## Slide 9
Verilator Simulation Output
Console evidence of successful loopback verification
UART TX/RX IP Core | VLSI Internship Project 9

## Slide 10
Conclusion & References
• The UART transmitter and receiver were successfully implemented as synchronous Verilog RTL IP blocks.
• The design uses FSM-based control, parameterized bit timing, start/stop-bit handling and 8-bit data transfer.
• Loopback simulation successfully transmitted and received both 0xA5 and 0x3C.
• EPWave analysis verified external data flow as well as internal FSM and counter behavior.
• The project demonstrates practical RTL design and functional verification concepts applicable to digital/VLSI design.
References
• IEEE Std 1364 — Verilog Hardware Description Language.
• Verilator Documentation — https://verilator.org/
• GTKWave — https://gtkwave.sourceforge.net/
• EDA Playground — https://www.edaplayground.com/
UART TX/RX IP Core | VLSI Internship Project 10